## Slide 1: Chapter 4
Textbook questions

## Slide 2
Convert each of the following decimal numbers to its binary equivalent.
37 (b) 93 (c) 129 (d) 355
Question 4-1
(a) 25=32 37-32=5
22=4 5-4=1
20=1
🡪100101

## Slide 3
(b) 26=64 93-64=29
24=16 29-16=13
23=8 13-8=5
22=4 5-4=1
20=1 1-1=0
1011101
(c) 27=128 129-128=1
20=1 1-1=0
🡪10000001

## Slide 4
(d) 28=256 355-256=99
26=64 99-64=35
25=32 35-32=3
21=2 3-2=1
20=1 1-1=0
🡪 101100011

## Slide 5: Question 4-2
Convert each of the following decimal numbers into binary-coded-decimal (BCD) numbers.
37
93
129
355
(a) 3 = 0011
7 = 0111
37 in BCD = 0011 0111
1001 0011
0001 0010 1001
0011 0101 0101

## Slide 6: Question 4-3
Based on your answer in 4-1 and 4-2, which is more efficient in expressing decimal numbers in the fewest number of bits, binary or BCD? Why is the less efficient coding scheme still very useful?

## Slide 7: Question 4-8
Three ADCs all have a range of 0 to 12V and a digitization uncertainty of ±1 LSB. What is the maximum uncertainty in the digitization of a 10-V signal if the converters have
8 bits?
12 bits?
16 bits?
(a) 28 = 256 so 12 V/256 = 0.047V
(b) 212 = 4096 so 12 V/4096 = 0.0029V
(c) 216 = 65536 so 12V/65536 = 0.00018V

## Slide 8: Question 4-11
ADCs digitalize at different rates. What conversion rate is required if a chromatographic peak is to be sampled and digitized 25 times between the first positive deflection from the baseline until the peak returns to the baseline? The total baseline-to-baseline time is (a) 20s and (b) 1s.

## Slide 9: Question 4-12
According to the Nyquist sampling criterion, a signal must be digitized at a rate at least twice that of the highest frequency in the signal to avoid a sampling error. If a particular 12-bit ADC has a conversion time of 5μs, what is the highest frequency that can be accurately digitized while satisfying the Nyquist criterion.